## Slide 1
`
`
1
3
2
Wiper contact
Wiper contact
2
3
1
What happens if we hook up only two legs of the potentiometer to our microcontroller?

## Slide 2
`
`
1
3
2
3
1
What happens if we hook up only two legs of the potentiometer to our microcontroller?
5V
5V
Microcontroller
Input pin
Leg 1 to Vcc
Leg 2 to the microcontroller’s analog input pin
Input pin
Microcontroller

## Slide 3
Inside microcontroller
Outside microcontroller
Pin A0
With microcontrollers, virtually no current flows into input pins
No voltage difference across potentiometer. Thus, no current.
No current through potentiometer means that voltage at the input pin (VA0) remains 5V regardless of potentiometer wiper position

## Slide 4
`
`
1
3
2
Wiper contact
Wiper contact
2
3
1
Let’s hook up the potentiometer to the microcontroller the correct way.
All three legs should have a connection.

## Slide 5
`
`
1
3
2
3
1
5V
5V
Microcontroller
Input pin
Leg 1 to Vcc
Leg 2 to the microcontroller’s analog input pin
Leg 3 to GND
Input pin
Microcontroller
GND
GND
Let’s hook up the potentiometer to the microcontroller the correct way.
All three legs should have a connection.

## Slide 6
Inside microcontroller
Outside microcontroller
Pin A0
Again, virtually no current flows into MCU input pins
Now, there’s a voltage difference across potentiometer. Current flows!
GND added
(connected to Leg 3 of the potentiometer )
Voltage divider created between R1 and R2 in potentiometer. So:
VA0=VCC * R2 / (R1 + R2)