## Slide 1
Open
This is our initial attempt at hooking up a switch to a microcontroller

## Slide 2
Open
What happens when we press the button?

## Slide 3
Button pressed!
Closed
The input pin becomes 5V

## Slide 4
Button pressed!
Closed
The input pin becomes 5V
digitalRead(2)returns HIGH

## Slide 5
But what does the input pin read when the button is not pressed?
Open
Button not pressed!

## Slide 6
But what does the input pin read when the button is not pressed?
The pin can oscillate between HIGH and LOW. This is called a floating pin!
Open
Button not pressed!

## Slide 7
Open
To solve the floating pin problem, you might think to add a GND connection

## Slide 8
Open
Add GND here
Added GND wire
To solve the floating pin problem, you might think to add a GND connection

## Slide 9
Open
Button not pressed!
Now, with the switch open, the input pin is 0V rather than floating
So, digitalRead(2)returns LOW
To solve the floating pin problem, you might think to add a GND connection

## Slide 10
Open
Button not pressed!
Now, with the switch open, the input pin is 0V rather than floating

## Slide 11
Open
Button not pressed!
Now, with the switch open, the input pin is 0V rather than floating
So, digitalRead(2)returns LOW

## Slide 12
Button not pressed!
Open
However… now what happens when we press the button?

## Slide 13
A short circuit!
This can damage our microcontroller
Closed
Button pressed!

## Slide 14
To avoid this short circuit condition and still prevent floating pins, we add what’s called a pull-down resistor

## Slide 15
This resistor “pulls down” the digital input pin to GND when the switch is open
Added pull-down resistor
To avoid this short circuit condition and still prevent floating pins, we add what’s called a pull-down resistor

## Slide 16
Button not pressed!
Now, with the switch open, the input pin is pulled down to 0V
Open

## Slide 17
Button not pressed!
Now, with the switch open, the input pin is pulled down to 0V
So, digitalRead(2)returns LOW
Open

## Slide 18
Button pressed!
And when switch closes, the input pin becomes 5V, and the pull-down resistor prevents a short circuit
So, digitalRead(2)returns HIGH
Closed