## Slide 1
With the switch open, the input pin is pulled up to 5V
Open

## Slide 2
With the switch open, the input pin is pulled up to 5V
So, digitalRead(2)returns HIGH
Open

## Slide 3
With the switch open, the input pin is pulled up to 5V
So, digitalRead(2)returns HIGH
Open
Button not pressed!

## Slide 4
Closed
And when switch closes, the input pin becomes 0V, and the pull-up resistor prevents a short circuit
So, digitalRead(2)returns LOW
Button pressed!
Yes, this is counterintuitive. With a pull-up resistor configuration, the input pin goes LOW when the button is pressed.