## Slide 1
Based on figures from: Platt, Make: Electronics, 1st Edition
Water Pressure ≈ Voltage (V) (measured in volts)
Water Flow ≈ Current (I) (measured in amps or A)
Hole width ≈ Resistance (R) (measured in ohms Ω)
Water level
As the water level increases, so too does the “pressure” of the water at the bottom of the tank (due to increasing amounts of weight), which will “push” more water out of the tank (increasing flow)
Hydraulic–electric analogy
Highest pressure
(at bottom of tank)
Lowest pressure
(at top of water level)
Lowest pressure
(negative terminal of battery)
Highest pressure
(positive terminal of battery)
0 volts
1.5 volts
R = 100Ω
I = 15mA
Current (I) flows from high to low pressure
The resistor resists the flow of current and the voltage (pressure) drops. The larger the resistor, the less current.
The resistor causes an electrical pressure (voltage) drop. So, the voltage is back to 0V here.