## Slide 1: ohm’s law
Ohm’s law
Based on: Scherz & Monk, Practical Electronics for Inventors, 3rd Edition; http://en.wikipedia.org/wiki/Hagen%E2%80%93Poiseuille_equation; http://hyperphysics.phy-astr.gsu.edu/hbase/electric/watcir2.html
F = flow rate in cm3 / sec
Poiseuille’s Law for fluids
I = charge flow rate in coloumbs/sec
Current is linearly proportional to the amount of voltage and resistance in circuit
circa ~1838
Ohm’s Law for electric circuits
circa ~1825
F
I
P1
P2
V2
V1
Pressure Drop
Notes: See also: https://youtu.be/HXOok3mfMLM?t=142 for an animation

## Slide 2
Based on: Scherz & Monk, Practical Electronics for Inventors, 3rd Edition; http://en.wikipedia.org/wiki/Hagen%E2%80%93Poiseuille_equation; http://hyperphysics.phy-astr.gsu.edu/hbase/electric/watcir2.html
F = flow rate in cm3 / sec
circa ~1838
Poiseuille’s Law for smooth flow (laminar flow) of fluids
Ohm’s Law for electric circuits
circa ~1825
F
I
P1
P2
V2
V1
Pressure Drop
Voltage Drop
I = charge flow rate in coulombs/sec
Resistance to flow R
Electrical resistance R
Poiseuille’s Law and Ohm’s law

High pressure
Low pressure
High potential
Low potential
Notes: See also: https://youtu.be/HXOok3mfMLM?t=142 for an animation

## Slide 4
How much current I is flowing through this circuit.
How much current I is flowing through this circuit.

## Slide 5
How much current I is flowing through this circuit.

## Slide 6
How much current I is flowing through this circuit.

## Slide 7
How much current I is flowing through this circuit.
How much current I is flowing through this circuit.
Solve for current I

## Slide 8
This entire wire is 0V because it directly touches the negative terminal of the battery.
This entire wire is 9V because it directly touches the positive terminal of the battery.
This entire wire is 0V because it directly touches the negative terminal of the battery.
This entire wire is 9V because it directly touches the positive terminal of the battery.
Step 1: Identify knowns

## Slide 9
This entire black wire is 0V, let’s represent it as node V2
This entire red wire is 9V, let’s represent it as node V1
This entire red wire is 9V, let’s represent it as node V1
This entire black wire is 0V, let’s represent it as node V2
V1
V2
V1
V2
Step 2: Apply knowns

## Slide 10
This entire black wire is 0V, let’s represent it as node V2
This entire red wire is 9V, let’s represent it as node V1
This entire red wire is 9V, let’s represent it as node V1
This entire black wire is 0V, let’s represent it as node V2
V1
V2
V1
V2
I = 90mA
I = 90mA
Step 3: Solve for Current I

## Slide 11
How much current I is flowing through this circuit.
How much current I is flowing through this circuit.
Solve for current I

## Slide 12
I = 50mA
Solve for Voltage Vcc
Vcc
Vcc = ?
0V
I = 50mA
?

## Slide 13
I = 1.32mA
Solve for Resistance R
9V
0V
I = 1.32mA
R=?
R=?

## Slide 14
Resistors in series vs. Parallel
Resistors in Series
Resistors in series divide voltage
Resistors in Parallel
Resistors in parallel divide current
I = 1.32mA
I = 4.5mA
RTotal = 2kΩ
We sum resistors in series:
Formula for the total resistance of parallel resistors:

## Slide 15
R1
R2
R3
Series Resistors
Current is the same across each resistor. Voltage is divided.
Parallel Resistors
Voltage is the same across each resistor. Current is divided.
R1
R2
R3

## Slide 16
R1
R2
R3
Resistors in Series
Components are in series if they are joined end-to-end (or head-to-tail) in sequence like this.
I

## Slide 17
Resistors in Parallel
Components are in parallel if their head’s share a node and their tail’s share a node.
R1
R2
R3
Node 1
Node 2
Node 1
Node 2

## Slide 18
Resistors in series vs. Parallel
I = 4.5mA
RTotal = 2kΩ
We sum resistors in series:
In this circuit, there are no branches and thus, we have the same current everywhere (there is no where else for the current to go). But we do get a voltage drop across each resistor.
In this circuit, we have a branch so the current gets divided. Both branches have the same resistance so current is divided evenly. We can calculate the current through each branch and sum.
ITotal
ITotal
I1
I2
VA = 9V
VB = 4.5V
VC = 0V
Voltage drop over R1
Voltage drop over R2
I = 4.5mA
Series Resistors
Current is the same across each resistor. Voltage is divided.
Parallel Resistors
Voltage is the same across each resistor. Current is divided.

## Slide 20
How much current I is flowing through this circuit.
How much current I is flowing through this circuit.
Solve for current I

## Slide 21
How much current I is flowing through this circuit.
How much current I is flowing through this circuit.
Step 1: Solve for total resistance
RTotal
1100Ω
RTotal
1100Ω
With series resistors, we sum resistances

## Slide 22
Step 2: Solve for Current I with aggregate resistance RTotal
RTotal
1100Ω
RTotal
1100Ω
I = 8.2mA
I = 8.2mA

## Slide 23
Solve for Current I
RTotal
3670Ω
RTotal
3670Ω
I = 8.2mA
I = 8.2mA

## Slide 24
Solve for voltage at VB
VA
VB
VC
VA
VB
VC
What is the voltage here?
What is the voltage here?

## Slide 25
VA = 9V
VB
VC = 0V
VA = 9V
VB
VC = 0V
How much current I is flowing through this circuit.
Step I: solve for current through circuit
How much current I is flowing through this circuit.

## Slide 26
VB
VB
VC
Step 2: Use current to calculate voltage drop across resistors
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R1
I = 36mA
I = 36mA
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R1

## Slide 27
VB
VB
Step 2: Use current to calculate voltage drop across resistors
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R2
I = 36mA
I = 36mA
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R2
VA = 9V
VC = 0V
VA = 9V
VC = 0V

## Slide 28
VB
VB
Step 3: Now Calculate VB
I = 36mA
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2
I = 36mA
I = 36mA
I = 36mA
VA = 9V
VC = 0V
VA = 9V
VC = 0V
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2
VB is equal to the battery’s positive terminal voltage minus the voltage drop over V1

## Slide 29
VB
VB
Voltage divider pattern
I = 36mA
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2
I = 36mA
I = 36mA
I = 36mA
VA = 9V
VC = 0V
VA = 9V
VC = 0V
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2

## Slide 30
VB
VB
Voltage divider pattern
I = 36mA
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2
I = 36mA
I = 36mA
I = 36mA
VA = 9V
VC = 0V
VA = 9V
VC = 0V
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2

## Slide 31
Voltage divider pattern
R1
GND
9V
R2
VB
VA
VC
R1
GND
V+
R2
Vout
Vin

## Slide 32
VA
VB
VC
VA
VB
VC
Step 3: Deterimine
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R1
I = 36mA
I = 36mA
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R1

## Slide 33
Step I: solve for current through circuit
VA
VB
VC
VA
VB
VC
How much current I is flowing through this circuit.
How much current I is flowing through this circuit.

## Slide 34
V
VA
VB
VC
VA
VB
VC
How much current I is flowing through this circuit.
I = 4.5mA

## Slide 35
ITotal
ITotal
ITotal
ITotal
Solve for ITotal

## Slide 36
ITotal
ITotal
I1
I2
ITotal
ITotal
Step 1: Observe that ITotal Splits into branches
I1
I2

## Slide 37
ITotal
ITotal
I1
I2
ITotal
ITotal
I1
I2
This red area is the same node, let’s call it Node A
This black area is the same node, let’s call it Node B
This black area is the same node, let’s call it Node B
This red area is the same node, let’s call it Node A
Step 2: Identify and name the nodes (junction points)

## Slide 38
ITotal
ITotal
I1
I2
ITotal
ITotal
I1
I2
This red area is the same node, let’s call it Node A
This black area is the same node, let’s call it Node B
This black area is the same node, let’s call it Node B
This red area is the same node, let’s call it Node A
Step 3: Define VA
VA = 9V
VA = 9V

## Slide 39
ITotal
ITotal
I1
I2
ITotal
ITotal
I1
I2
VA
9V
VA
9V
Step 3: Solve for I1 and I2

## Slide 40
ITotal
ITotal
I1
I2
ITotal
ITotal
I1
I2
VA
9V
VA
9V
Step 3: Solve for I1 and I2

## Slide 41
ITotal
ITotal
I1
I2
ITotal
ITotal
I1
I2
This red area is the same node, let’s call it VA
This black area is the same node, let’s call it VB
This black area is the same node, let’s call it VB
This red area is the same node, let’s call it VA
Step 3: Solve for I1 and I2