## Slide 1
Resistors in series vs. Parallel
Resistors in Series
Resistors in series divide voltage
Resistors in Parallel
Resistors in parallel divide current
I = 1.32mA
I = 4.5mA
RTotal = 2kΩ
We sum resistors in series:
Formula for the total resistance of parallel resistors:

## Slide 2
R1
R2
R3
Series Resistors
Current is the same across each resistor. Voltage is divided.
Parallel Resistors
Voltage is the same across each resistor. Current is divided.
R1
R2
R3

## Slide 3
R1
R2
R3
Resistors in Series
Components are in series if they are joined end-to-end (or head-to-tail) in sequence like this.
I

## Slide 4
Resistors in Parallel
Components are in parallel if their head’s share a node and their tail’s share a node.
R1
R2
R3
Node 1
Node 2
Node 1
Node 2

## Slide 5
Resistors in series vs. Parallel
I = 4.5mA
RTotal = 2kΩ
We sum resistors in series:
In this circuit, there are no branches and thus, we have the same current everywhere (there is no where else for the current to go). But we do get a voltage drop across each resistor.
In this circuit, we have a branch so the current gets divided. Both branches have the same resistance so current is divided evenly. We can calculate the current through each branch and sum.
ITotal
ITotal
I1
I2
VA = 9V
VB = 4.5V
VC = 0V
Voltage drop over R1
Voltage drop over R2
I = 4.5mA
Series Resistors
Current is the same across each resistor. Voltage is divided.
Parallel Resistors
Voltage is the same across each resistor. Current is divided.

## Slide 7
How much current I is flowing through this circuit.
How much current I is flowing through this circuit.
Solve for current I

## Slide 8
How much current I is flowing through this circuit.
How much current I is flowing through this circuit.
Step 1: Solve for total resistance
RTotal
1100Ω
RTotal
1100Ω
With series resistors, we sum resistances

## Slide 9
Step 2: Solve for Current I with aggregate resistance RTotal
RTotal
1100Ω
RTotal
1100Ω
I = 8.2mA
I = 8.2mA

## Slide 10
Solve for Current I
RTotal
3670Ω
RTotal
3670Ω
I = 8.2mA
I = 8.2mA

## Slide 11
Solve for voltage at VB
VA
VB
VC
VA
VB
VC
What is the voltage here?
What is the voltage here?

## Slide 12
VA = 9V
VB
VC = 0V
VA = 9V
VB
VC = 0V
How much current I is flowing through this circuit.
Step I: solve for current through circuit
How much current I is flowing through this circuit.

## Slide 13
VB
VB
VC
Step 2: Use current to calculate voltage drop across resistors
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R1
I = 36mA
I = 36mA
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R1

## Slide 14
VB
VB
Step 2: Use current to calculate voltage drop across resistors
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R2
I = 36mA
I = 36mA
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R2
VA = 9V
VC = 0V
VA = 9V
VC = 0V

## Slide 15
VB
VB
Step 3: Now Calculate VB
I = 36mA
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2
I = 36mA
I = 36mA
I = 36mA
VA = 9V
VC = 0V
VA = 9V
VC = 0V
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2
VB is equal to the battery’s positive terminal voltage minus the voltage drop over V1

## Slide 16
VB
VB
Voltage divider pattern
I = 36mA
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2
I = 36mA
I = 36mA
I = 36mA
VA = 9V
VC = 0V
VA = 9V
VC = 0V
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2

## Slide 17
VB
VB
Voltage divider pattern
I = 36mA
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2
I = 36mA
I = 36mA
I = 36mA
VA = 9V
VC = 0V
VA = 9V
VC = 0V
V1=3.6V
Voltage drop over R1
V2 =5.4V
Voltage drop over R2

## Slide 18
Voltage divider pattern
R1
GND
9V
R2
VB
VA
VC
R1
GND
V+
R2
Vout
Vin

## Slide 19
R1
GND
V+
R2
Vin
Vout
Vout
Vin
We know the voltage drop over R2 is equal to Vout , which is also equal to I * R2
We also know that Vin is equal to VR1 + VR2
Using Ohm’s Law, we can substitute VR1 + VR2 with I * R1 + I * R2
Rearrange equation using algebra
Now substitute for I in Vout = I * R2
Rearrange to popular formulation:
Deriving the voltage divider equation
Notes: https://www.khanacademy.org/science/electrical-engineering/ee-circuit-analysis-topic/ee-resistor-circuits/a/ee-voltage-divider

## Slide 20
Vin
R1
R2
RLoad
Vout

## Slide 21
VA
VB
VC
VA
VB
VC
Step 3: Deterimine
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R1
I = 36mA
I = 36mA
I = 36mA
V1
Voltage drop over R1
V2
Voltage drop over R1

## Slide 22
Step I: solve for current through circuit
VA
VB
VC
VA
VB
VC
How much current I is flowing through this circuit.
How much current I is flowing through this circuit.

## Slide 23
V
VA
VB
VC
VA
VB
VC
How much current I is flowing through this circuit.
I = 4.5mA

## Slide 24
ITotal
ITotal
ITotal
ITotal
Solve for ITotal

## Slide 25
ITotal
ITotal
I1
I2
ITotal
ITotal
Step 1: Observe that ITotal Splits into branches
I1
I2

## Slide 26
ITotal
ITotal
I1
I2
ITotal
ITotal
I1
I2
This red area is the same node, let’s call it Node A
This black area is the same node, let’s call it Node B
This black area is the same node, let’s call it Node B
This red area is the same node, let’s call it Node A
Step 2: Identify and name the nodes

## Slide 27
ITotal
ITotal
I1
I2
ITotal
ITotal
I1
I2
This red area is the same node, let’s call it Node A
This black area is the same node, let’s call it Node B
This black area is the same node, let’s call it Node B
This red area is the same node, let’s call it Node A
Step 3: Define VA
VA = 9V
VA = 9V
+
-
+
-

## Slide 28
ITotal
ITotal
I1
I2
ITotal
ITotal
I1
I2
VA
9V
VA
9V
Step 4: Solve for I1 and I2
+
-
+
-

## Slide 29
ITotal
ITotal
I1
I2
ITotal
ITotal
I1
I2
VA
9V
VA
9V
Step 5: Solve for ITotal
+
+
-
+
-

## Slide 30
ITotal
ITotal
I1
I2
ITotal
ITotal
I1
I2
This red area is the same node, let’s call it VA
This black area is the same node, let’s call it VB
This black area is the same node, let’s call it VB
This red area is the same node, let’s call it VA
Step 3: Solve for I1 and I2