## Slide 3
Notes: Chart from: https://robot-r-us.com.sg/p/circuit-playground-express

## Slide 4
CPX Input
Left Button
Right Button
Temperature Sensor
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour

## Slide 5
Circuit express playground hardware
CPX Board
Built-in output
Built-in sensors/input

## Slide 6
Built-in CPX Input
Left Button
Right Button
Temperature Sensor
Microphone
Slide Switch
Infrared (IR) Receiver
Accelerometer
(motion sensor)
(sound sensor)
Light Sensor
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour

## Slide 7
CPX Input
Left Button
Right Button
Temperature Sensor
Microphone
Slide Switch
Infrared (IR) Receiver
Accelerometer
(motion sensor)
(sound sensor)
Light Sensor
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour

## Slide 8
Alligator Connection Pads
Speaker
(sound output)
Infrared (IR) Transmitter
NeoPixel RGB LEDs
(10 total)
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour

## Slide 9
Speaker
(sound output)
Infrared (IR) Transmitter
NeoPixel RGB LEDs
(10 total)
Alligator Connection Pads
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour

## Slide 10
Alligator pads
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour

## Slide 11
Analog Input
A1
Input Range: 0-1023
A2
Input Range: 0-1023
A3
Input Range: 0-1023
A4 Input Range: 0-1023
A5 Input Range: 0-1023
A6 Input Range: 0-1023
A7 Input Range: 0-1023
In MakeCode, you can use A1-A7 as analog input, which converts a voltage to a number between 0-1023 (using a 10-bit ADC)
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour

## Slide 12
Alligator Pads
(14 total; There are different pad types, including for power, I/O, I2C)
14 Alligator Connection Pads
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour

## Slide 13
14 Alligator Connection Pads
GND
GND
GND
3.3V
3.3V
Power Source Vout
A1 / D6
GPIO Pin
A0 / D12
GPIO Pin
A2 / D9
GPIO Pin
A3 / D10
GPIO Pin
A4 / D3 GPIO Pin + SCL
A5 / D2 GPIO Pin
A6 / D0 GPIO Pin + Serial Receive
A7 / D1 GPIO Pin + Serial Transmit
The 14 connection pads allow you to power and connect to external components like other buttons, LEDs, etc.
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour

## Slide 14
POWER Pads
https://learn.adafruit.com/adafruit-circuit-playground-express/pinouts
GND
GND
GND
3.3V
3.3V
Power Source Vout
If connected to USB, will be 5V out. If connected to LiPoly battery, will be battery’s Vout (3.7V). If connected to both, will default to higher voltage source. You can draw 500mA continuous up to 1mA peak, so great for NeoPixels or other higher-load components.
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour
https://learn.adafruit.com/adafruit-circuit-playground-express/pinouts

## Slide 15
Input/Output pads
All I/O pads can be used as digital I/O and analog input (10-bit ADC). All but A0 can be used for capacitive touch. Each pad is 3.3V and can provide up to ~20mA of current.
A1 / D6
Digital I/O, analog in, PWM out.
Has PWM output. Supports capacitive touch.
A0 / D12
Digital I/O and analog I/O. A special pin that can do true analog output so great for playing audio clips. Cannot be used for capacitive touch.
A2 / D9
Digital I/O, analog in, PWM out.
Supports capacitive touch.
A3 / D10
Digital I/O, analog in, PWM out.
Supports capacitive touch.
A4 / D3
Digital I/O, analog in, PWM out.
Supports capacitive touch. Also, the I2C SCL pin.
A5 / D2
Digital I/O, analog in, PWM out.
Supports capacitive touch. Also, the I2C SDA pin.
A6 / D0
Digital I/O, analog in, PWM out.
Supports capacitive touch. Also, the Serial Receive pin.
A7 / D1
Digital I/O, analog in, PWM out.
Supports capacitive touch. Also, the Serial Transmit pin.
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour

## Slide 16
Capacitive Touch Sensor Pads
A1
Supports capacitive touch.
A2
Supports capacitive touch.
A3
Supports capacitive touch.
A4
Supports capacitive touch.
A5
Supports capacitive touch
A6
Supports capacitive touch.
A7
Supports capacitive touch.
Notes: https://learn.adafruit.com/adafruit-circuit-playground-express/guided-tour

## Slide 17
Makey Makey Activity
Notes: https://krisswanson.blog/2017/05/05/circuit-circuit-a-makey-makey-like-setup-for-the-adafruit-circuit-playground/